## Slide 1: XO3L PCB breakout recommendation
May 22, 2014
Packaging Solutions

## Slide 2: PCB breakout recommendations
For 0.8 mm pitch XO3L 400caBGA used as example
PCB 62 mils thick
No blind/buried vias
½ oz. Cu planes
SMT assembly marks included
Good, Better & Best are based on IPC7351 Land Variation for collapsing ball, applying rule for 0.45mm nominal ball diameter (0.40mm -0.30mm)
Product Offering | XO3L-69C-400caBGA, 17x17 mm package, 0.8 mm package ball pitch |  | 
PCB Breakout Option # | Good | Better | Best
MAX # of signal layers | 4 | 4 or more | 4
ball pad diameter (mils) | 16 | 14 | 12
ball pad opening (mils) | 21 | 18 | 17
trace width (mils) | 6 | 4 | 4
trace spacing (mils) | 4 | 4 | 3
via diameter (mils) | 10 | 10 | 6
via land diameter (mils) | 18 | 18 | 14
# of User IO | 336 (100%) | 336 (100%) | 336 (100%)
Comments | VCCIOs and VCC tied to plane. Decoupling capacitors at bottom layer for VCCIOs and VCC | VCC tied to plane. Decoupling capacitors at bottom layer for VCC. VCCIOs are routed at signal layers. | VCCIOs and VCC tied to plane. Decoupling capacitors at bottom layer for VCCIOs and VCC

## Slide 3: PCB breakout recommendations
For 0.5 mm pitch XO3L 324fcCSP as example
Product Offering | XO3L-69E-324fcCSP, 10x10 mm package, 0.5 mm package ball pitch |  | 
PCB Breakout Option # | Easiest | Better | Best
MAX # of signal layers | 4 or more | 4 or more | 6
ball pad diameter (mils) | 16 | 12 | 14
ball pad opening (mils) | 16 | 12 | 12
trace width (mils) | 4 | 4 | 4
trace spacing (mils) | 3.8 | 3.4 | 3.8
via diameter (mils) | 8 | 5 | 4
via land diameter (mils) | 12 | 8.8 | 8
# of User IO | ~50% | 282 (100%) | 282 (100%)
Comments | No blind vias. Not all bga pads are connected. | No blind vias. Low cost due to via offset. | Microvia and blind via Via-in-pad
PCB 62 mils thick
Vias are to be non- conductive epoxy filled, flat surface at top land
½ oz. Cu planes
SMT assembly marks included
Good, Better & Best are based on IPC7351 Land Variation for non- collapsing ball, applying rule for 0.30mm nominal ball diameter (0.40mm -0.30mm)

## Slide 4: PCB breakout recommendations
For 0.4 mm pitch XO3L 81wlcsp as example
Product Offering | XO3L-43E-81wlcsp, 3.7x3.8 mm package, 0.4 mm package ball pitch | 
PCB Breakout Option # | Better | Best
MAX # of signal layers | 4 | 4
ball pad diameter (mils) | 12 | 10
ball pad opening (mils) | 12 | 10
trace width (mils) | 3 | 4 (3)
trace spacing (mils) | 2.3 | 4 (3)
via diameter (mils) | 4 | 4
via land diameter (mils) | 8 | 8
# of User IO | Max I/O | Max I/O
Comments | Through via; Microvia | Microvia & blind vias Via-in-pad offset for some areas to meet 4mils trace/space. Can also use 3 mils trace/space
PCB 62 mils thick
Vias are to be non- conductive epoxy filled, flat surface at top land
½ oz. Cu planes
SMT assembly marks included
Better & Best are based on IPC7351 Land Variation for non- collapsing ball, applying rule for 0.25mm nominal ball diameter (0.35mm -0.25mm)